## Slide 1: Architecture of IoT Platform
2015.06.26.
Team 5

## Slide 2: Agenda
Project Context
Architectural Driver
System Context
Architectural Design
Detail Design
Test
Time log
Future plan
Lessens & Learned

## Slide 3: Project Context
Business Context
  Strategy
    Building “IoT Ecosystem Infrastructure” to provide benefits to stakeholders.
    . Easy installation for IoT nodes
    . Utilizing cost competitive IoT products
  Future direction
    Provide a standard framework to facilitate 3rd party application development
    Support future data mining & analysis
  Profit Model
    Receive fee from the app. developer according to their permission of access level
    The expansion of ecosystem brings more profits
Market Context
  Time to market
    This product should be developed and delivered within 5 weeks.

## Slide 4: Project Context
Technical Context
  Should support machine-to-person interaction model(M2P) and machine-to-machine(M2M) interaction models.
  The system has to support IoT nodes at least 10 years.
  Privacy and security are required considerations for IoT Environment
  System should make it easy to add emerging protocols.
Elements | Terminal | System | SA Node
Device Type | Mobile and PC | Server (PC) | Sensor, Actuator
Language | Java | Java | Arduino Language
Development Tools | Eclipse IDE | Eclipse IDE | Arduino IDE

## Slide 5: Project Context
Organizational Context
  The team is composed with 6 members
    Design : all together
    Test and verification : each member who developed the component will do unit test and verification
    Integration test : all together
    Responsibility
  Organizational Culture
    Members will be responsible and accountable for their individual area.
    Stand-up meeting at each day before starting work.
    Facilitate collaboration and team building through group lunch approach.
    Work 5 days a week for 5 weeks
Management
Jongsoo Oh
Developer(Server)
Youngsoo Choi
Developer(Node)
Sangjun Jung
Developer(Terminal)
Swapan Pati
Architectural Design
Hoejung Yun
Architectural Design
Jinsuk Oh

## Slide 6: Architectural Driver
Functional Requirement (1/2)
ID | Requirement | Description
R-01 | Control SA Nodes | Users can determine the temperature/humidity, turn on and off lights, open and close the door, turn on the alarm, and determine if anyone is home.
R-02 | Give the information about installed Nodes and sensors/actuators | User can get the information how many nodes are installed at the system and what sensors/actuators are installed on each node.
R-03 | Store the sensor value of node | System should store sensor values.
R-04 | Store log for user commands | System should log all user commands.
R-05 | Review stored data | User should review their sensor and command history.
R-06 | Send emergency message | The system should send an emergency message when the door is manually opened while alarmed or the house is suddenly occupied while alarmed.
R-07 | Disable door opening automatically | The system should not allow automatic door opening while the house is alarmed. The alarm must be disabled prior to opening the door.

## Slide 7: Architectural Driver
Functional Requirement (2/2)
ID | Requirement | Description
R-08 | Support alarm message | The system should send a message to the user to inform them when the house is vacant and not alarmed.
R-09 | Ask for alarming home | When the house is vacant and not alarmed the system should ask users if they want to alarm the home.
R-10 | Locking automatically | When the house is vacant and not alarmed and the user do not respond within 5 minutes, the house will lock itself and close the door if opened.
R-11 | Automatically turn off the light | The system should automatically turn off the lights when no one is home and 10 minutes elapses.
R-12 | Add/Remove SA Node | Users can add and remove nodes the system without having to restart the system or other nodes

## Slide 8: Architectural Driver
Quality Attribute
ID | Priority | Description | Attribute
QA-01 | High | Installer can add and remove nodes to the system easily. | Usability
QA-02 | Medium | System will be available always to do any IoT Based Operations | Availability
QA-03 | High | Do not allow unauthorized persons to register a sensor | Security
QA-04 | Medium | Only the authorized person can access the home sensors/actuators or access any data generated by them, or any data stored in the system. | Security
QA-05 | Low | The system should store sensor values and log all user commands for some period of time | Reliability
QA-06 | High | The system should make it easy for application developers | Extensibility
QA-07 | Medium | The system should make it easy to add emerging protocols | Modifiability

## Slide 9: Architectural Driver
Business Constraints
Technical Constraints
Consideration | Description
Schedule limitations | All features of functional requirements list should be implemented by 26th June.
Consideration | Description
Computer language(s) | The system only permits Java language.
Logistical Issues | The system should store sensor values and log all user command, and time limitation is up to max. 72 hours.
Communication | CMU Network should be always available

## Slide 10: System Context
Terminal
SA node
Server
Project scope
SA node
Terminal
Node
Terminal
3rd party
vendors
Terminal
Mail Box
Node
Home Security
Node

## Slide 11: Architecture Design - Level 1
Apply Server-Client pattern for loose coupling
Dynamic
Notes: Rationale : SRP(Single Responsibility Principle)을 고려하여 Element를 IoT Service, Node and Terminal로 나누어 Element간의 loose coupling되도록 설계하고, Element간의 상호 작용 시에도 coupling을 줄이기 위하여 message를 통하여 상호 작용하는 방법으로 설계하기 위하여 Server-Client Pattern의 주요 message exchange pattern(MEP)인 request-response pattern과 one-way pattern을 alternatives 검토하였음.
Iot Service, Node and Terminal 사이에는 service request와 requested service 수행 및 그에 대한 response가 Requirements이므로 one-way pattern보다는 request-response pattern을 적용하여 IoT Service와 Node/Terminal간의 relationship을 갖도록 design decision 하였음.

## Slide 12: Architecture Design - Level 1
Rationale
In view of SRP (Single Responsibility Principle), we divided the responsibility (loose coupling) into three Elements (IoT Service, Node & Terminal).
Message Exchange Pattern (MEP) of Server-Client Pattern has been considered for interaction between Elements. In MEP, we have considered “Request-Response Pattern” over “One-Way Pattern” because “IoT Service” has to Response based on “Terminal”/”Node” Service Request.
Table 1. Element Responsibility Catalog for the First-Level Decomposition
 | Perspective: Dynamic
Element | Responsibilities
Iot Service | Iot Service act as a Server & is responsible to Interact & manage the Clients(Node & Terminal)
Node | Node act as a Client & responsible for Node core operation. It has to process/response Iot Service command
Terminal | Terminal act as a Client & responsible for Terminal core operation. It has to process/response Iot Service command

## Slide 13: Architecture Design - Level 2
Apply Layered Architecture Pattern For QA6
Extensibility - The system should make it easy for application developers
Dynamic
Notes:   Rationale:
    QA6에서 도출된 The system should make it easy for application developers를 IoT service 의 extensibility 확보 하기 위해서 약속된 규약(Protocol)을 통한 message 전송과 수신을 할 수 있는 부분을 독립적으로 구성
    이는 앞에서 언급한 Request–response pattern을 적용하여 대외적인 관계를 추상화하여 처리한 수 있음
    그리고, Layered architecture pattern을 적용하여 각자의 지원 기능인 Service와 상호작용을 위한 Message Handler의 역할을 restrict dependency를 추구할 수 있음
    대내적으로는 Message handler 부분을 Library 형태로 지원하여 node & service 개발 시 service 들이 porotocol message를 자세하게 알지 않아도 개발 가능하도록 지원하여 개발용이성 확보

## Slide 14: Architecture Design - Level 2
Rationale:
  In Level-2 we have decomposed the elements further by considering the QA6 (Extensibility).
  In Level-1 “Request-Response Pattern”, abstracting the external relationship, here applied “Layered Pattern” where “Handler” will interact with respective Elements Services (Internal relationship) whereas; same Handler will do External Elements Interactions.
  Handler will be in Library form (Hide the Data Marshaling/Un-marshaling & Security) for Message External Interaction (Protocol based), with this ensuring the ease of development for Node & Terminal
Table 2. Element Responsibility Catalog for the Second-Level Decomposition
 | Perspective: Dynamic
Element | Responsibilities
Service | Responsible for Process core operation apart from external data communication
Handler | Externaly, Handler is responsible for data communication with other device. Internaly, Handling the data communication via own defined protocol.

## Slide 15: Architecture Design - Level 3
Add component and Apply Pipe & Filter pattern for QA3,QA7
Security : Do not allow unauthorized persons to register a sensor
Modifiability : The system should make it easy to add emerging protocols
Dynamic
Notes:   이번 decomposition의 경우 QA3(“Do not allow unauthorized persons to register a sensor“)의 security와 QA7(“System should make it easy to add emerging protocols”)의 modifiability를 확보하기 위함
  Level2의 (Message) Handler component는 각 기기의 message 송수신을 담당하게 된다.
  하지만, 각 기기 간의 message 보안을 위해서 security 담당할 component를 구성
  이 security component는 Encrypt data tatic을 적용하여 message 암호화를 위한 security key의 발행과 message 암호화/복호화를 지원하여 system내 message security 확보
  Security component에서 복호화 된 data를 protocol component에서 반복적으로 무의미한 command 전달 시 악의적 attack 으로 간주하여 closing a port(Limit access tatic) 처리하여 system 보호함
  추가적으로 WIFI socket 이 외의 다른 통신 방식을 지원하기 위해서 transport 담당할 componet를 추가적으로 구성하여 다른 통신 방식 지원할 수 있도록 함
  이 transport component는 각 기기 간의 session 연결과 message 송수신을 담당
  수신 시 transport component에서 받은 message를 security component에서 복호화, porotocol component에서 의미 있는 단위로 나눠 service로 전달
  해당 decomposition의 경우 적용 가능한 pattern에 대해서 검토했으나 적용 가능한 pattern보다는 QA를 지원하기 위한 component 추가를 통하여 decomposition 함
  component 추가와 함께 구조적으로 Pipe & Filter pattern을 적용하여 추후 새로운 security policy 적용이나 emerging protocol 적용하기 용이 하도록 design decision 함
  Apply data security for making the robust system we applied the Pipe & Filter Pattern to achive it.
  Apply Transport component for making the connection type(WIFI, BT etc) loosely couple with the system. In here to achive it we applied the Pipe & Filter Pattern

## Slide 16: Architecture Design - Level 3
Rationale:
  In level-3 decompose further by considering the QA3 (Security) & QA7 (Modifiability)
  In Level-2, Handler component is made responsible for message send & receive from each Elements.
  Handler decomposed further into security (Encrypt data tatic applied) component for making the robust secure system.
  Handler decomposed further into Transport component for making the connection type(Socket) (WIFI, BT etc) loosely couple with the system.
  Protocol component will do the data formatting (Marshaling/Un-marshaling)
  By applying the component additional structurally Pipe & Filter pattern, to design decision to be easier to apply future of the new security policy applied and emerging protocol additions.
Table 3.1. Element Responsibility Catalog for the Second-Level Decomposition
Associated Drawings: Figure 3 | Perspective: Dynamic
Element | Responsibilities
Service | Service is managing the core functionality of the running process.
Protocol | This component is responsible formating the message for communication.
Security | This component is responsible for incoming/outgoing data Encoding & Decoding based on project defined Encription Logic.
Transport | This is responsible for making the data external communicaiton with barrier(WIFI, BT etc) independent & loose couple

## Slide 17: Architecture Design - Level 3
Switch to physical perspective
Rationale:
  Security 강화와 infrastructure 비용 감소를 위해서 Server의 위치를 Home network 안쪽으로 결정함
  사용자 log와 login에 대해서 local로 관리하기 때문에 외부에 server가 있는 것보다는 security 확보 가능
  AP에 Server를 Embedded하는 것도 고려 가능하며, 이러한 경우 Cost 절감 효과를 가질 수 있음.
Network
Component
Database storage
Legend
Part of device
Device
Physical

## Slide 18: Architecture Design - Level 4
Apply Broker Pattern for QA1
Usability : Installer can add and remove nodes to the system easily.
Dynamic
Notes: QA1(“Easy Node Registration/UnRegistration”)에서 도출된 Usability를 만족시키기 위하여 Node Registration/Unregistration 절차가 간단하고 복잡하지 않도록 IoT Service, Node/Terminal간의 상호작용을 간단하게 design해야 할 필요성이 있으며, 이를 위하여 Broker Pattern과 Publish-Subscribe Pattern을 alternatives로 검토 하였음.
Publish-Subscribe Pattern의 경우 Less control over ordering of messages, delivery of message is not guaranteed등의 약점이 있으며, Broker Pattern의 경우 Terminal과 Node 상호작용 시에 직접적이 아닌 Broker를 통하여 상호작용을 하므로 Location Transparency의하여 상호작용 절차가 간단해 질 수 있는 장점이 있음.
또한 Broker Pattern에서는 Broker에서 message ordering 및 guarantee of message delivery가 가능하므로 Level 1에서 적용된 Server-Client Pattern의 MEP(Message Exchange Pattern)과 함께 적용하는 것이 좀 더 효과적인 것으로 판단하여 Broker Pattern을 적용하는 것으로 design decision 함.

## Slide 19: Architecture Design - Level 4
Rationale:
  In Level-4, we have decomposed further by considering QA1 (Usability). Easy Node Registration/Un-Registration procedure simple in order to satisfy the design, Interaction between IoT Service and Node/Terminal we used Broker Pattern.
  Broker is hide the data flow Transparency(ignorant of the identity,location & characteristics) so its easy for user to do Registration/Un-Registration with minimal steps & indirectly benifit for the developer.
  We considered Broker Pattern because it allows message ordering and the guarantee of message delivery in the Broker, be applied in conjunction with the applied Server-Client Pattern of MEP (Message Exchange Pattern) from Level 1 and a more effective to design decision that is to apply the decision to Broker Pattern
Table 4.1. Element Responsibility Catalog for the Second-Level Decomposition
 | Perspective: Dynamic
Element | Responsibilities
Broker | Broker is an intermediary which receives a message from the sender(Terminal or Node) and routes a message to proper destination(Terminal or Node).

## Slide 20: Architecture Design - Level 5
for QA4
Extensibility : The system should make it easy for application developers
Dynamic
Notes:   Broker로부터 전달받은 Message를 모든 Node/Terminal로 전달하여 처리 될 수 있음을 고려하고 Node/Terminal이 Runtime시에 add/remove될 수 있는 동작 환경에서도 Node/Terminal에 Message전달/처리가 되어야 함을 고려하여 Publish-Subscribe Pattern을 적용하여 Node Mgr, Terminal Mgr를 추가 함.
  QA4의 “Only the authorized person can access the home sensors/actuators or access any data generated by them, or any data stored in the system.”에서 도출된 Security를 만족하기 위하여 Security Attack에 대하여 Security Tactics 중에서 Resist Attacks Tactics의 Identify Actors, Authetificate Actors, Authorize Actors를 적용하기 위해 Component(Auth Mgr)를 추가하여 Terminal의 Login, Permission 관리를 하도록 함

## Slide 21: Architecture Design - Level 5
Rationale:
  All Messages that have been transmitted from the Broker in consideration of the fact that it can be processed and is transferred to the Node / Terminal, Node / Terminal can be added/remove Runtime in the operating environment that can be the take the control in mind, by applying the Publish-Subscribe Pattern we decomposed into Node Management, and Terminal Manager.
  In considering QA4 “Only the authorized person can access the home sensors / actuators or access any data generated by them, or any data stored in the system." It is in the Security Tactics for Security Attack in order to satisfy the Security that has been derived in Resist Attacks Tactics of Identify Actors, Authetificate Actors, in order to achive it, we added an Auth Manager component, so only Authorize persons will allowed to access the system
Table 5.1. Element Responsibility Catalog for the Second-Level Decomposition
 | Perspective: Dynamic
Element | Responsibilities
Node Manager | Managing the Node Informations (Registred Node Details, Node Data (Sensors, Acturators & Services)
Terminal Manager | Managing the Terminal Information (Logged In Terminal Details)
Auth Manager | Responsible for validating the Terminal user details & generate the session Key for valid connected users.Managing the session for active connection
Log DB | Repository for keeping all connected Node data (Sensors data) as well as Terminal command (Actuator Actions) history
Login DB | Keeping all Registred Users (Terminal) Login User ID & Password Details

## Slide 22: Architecture Design - Level 6
Node & Terminal Decomposition
Dynamic
Notes:   Terminal과 Node의 경우 기존에 분리된 Protocol, Security, Transport component 즉 Message Hanlder를 공유하며 이를 통해 안정적이고 보안이 유지된 message 송수신 할 수 있음
  이와 함께 Terminal과 Node의 고유의 동작을 위한 component 추가
  Terminal은 MVC pattern을 적용하여 사용자의 UX를 지원하기 위한 View component를 독립적으로 구성
  이를 통해 UX변경 시 변경 영향도 최소화
  Node의 주요 기능인 Sensor/Actuator/Service는 개별적 기능으로 Single Responsibility Principle 적용 분리된 component로 추가
  이를 통해 3rd party node 개발자들은 개발이 필요한 component만 개발하면 되기 때문에 개발 용이

## Slide 23: Architecture Design - Level 6
Rationale:
  Considering the Functional requirement, added components for the specific behavior of the Terminal & Node.
  Terminal applies the MVC pattern, individually View component to support the user's UX setting by this, minimize the impact of change on UX change.
  The main function of Node divided to Node Sensor / Actuator / Service is, added to the Single Responsibility Principle applied separate component in a separate responsibility. Thus, 3rd party node developer, since it is sufficient to develop only the necessary component development, easier to develop
Table 6.1. Element Responsibility Catalog for the Second-Level Decomposition
 | Perspective: Dynamic
Element | Responsibilities
View | Responsible for User Input & data presentation (Specially for UI scenerio)
Sensor Manager | Responsible for Handling the connected Sensors into the Node
Actuator Manager | Responsible for Handling the connected Actuators into the Node
Service Provider | Responsible for providing servie such as data mining and actutor handling.

## Slide 24: Architecture Design - Final dynamic perspective

## Slide 25: Architecture Design - Final physical perspective
Network
Component
Database storage
Legend
Part of device
Device

## Slide 26: Architecture Design - Final static perspective
Node
Terminal
IoT service
A
B
B
A
B
A
B
A
Interface
Composition
Aggregation
Class
Use
Realize
IoTMiddleWare
Legend

## Slide 27
Detail Design

## Slide 28: Detail Design
IoT service
Node
Terminal
A
B
B
A
B
A
B
A
Interface
Composition
Aggregation
Class
Use
Realize
Package
Legend

## Slide 29: Detail Design - IoT Service
A
B
B
A
B
A
B
A
Interface
Composition
Aggregation
Class
Use
Realize
Package
Legend

## Slide 30: Detail Design - IoT Service(Responsibility Catalog) #1
Table D1. Element Responsibility Catalog for IoT Service detail design
 | Perspective: Static
Element | Responsibilities
Service | Service is managing the core functionality of the running process.
Brocker | Broker is an intermediary which receives a message from the sender(Terminal or Node) and routes a message to proper destination(Terminal or Node).
MessageRouter | MessageRouter is managing the Message Routing table which will transfer the messages to intended elements (NodeManager, TerminalManager) after getting from Broker & vice versa.
NodeManager | Managing the Node Informations (Registred Node Details, Node Data (Sensors, Acturators & Services)
TerminalManager | Managing the Terminal Information (Logged In Terminal Details)
AuthManager | Responsible for validating the Terminal user details & generate the session Key for valid connected users.Managing the session for active connection
DataManager | Managing the database operatation. Keeping the DB Abstarction from NodeMangaer,TerminalManager & AuthManager.
MessageHandler | Responsible for Overall IotMiddleware management. Handling the message filteing from network to protocol (Transport<-->Security<-->Protocol) & Transfer the filtered message to Service for operation
Protocol | This component is responsible formating the message for communication.

## Slide 31: Detail Design - IoT Service(Responsibility Catalog) #2
Table D2. Element Responsibility Catalog for IoT Service detail design
 | Perspective: Static
Element | Responsibilities
Security | This component is responsible for incoming/outgoing data Encoding & Decoding based on project defined Encription Logic.
Transport | This is responsible for making the data external communicaiton with barrier(WIFI, BT etc) independent & loose couple
WifiTransport | Managing the Wifi Socket operation(open/close socket, read/write operation )

## Slide 32: Detail Design - Terminal
A
B
B
A
B
A
B
A
Interface
Composition
Aggregation
Class
Use
Realize
Package
Legend

## Slide 33: Detail Design - Terminal(Responsibility Catalog)
Table D3. Element Responsibility Catalog for Terminal detail design
Associated Drawings: Figure 3 | Perspective: Static
Element | Responsibilities
Service | Service is managing the core functionality of the running process.
SensorManager | Responsible for Handling the connected Sensors into the Node
ActuatorManager | Responsible for Handling the connected Actuators into the Node
ServiceProvider | Responsible for providing servie such as data mining and actutor handling.
MessageSendable | Message를 server로 전달 할 수 있는 interface
RuleChecker | Service에 대한 rule을 check하는 루틴으로 dataAnalyzer를 통해서 정제된 data를 통해 원하는 rule이 만족될 경우 그에 대한 message를 생성 및 전달
DataAnalyzer | Log나 command에 대해서 받아서

## Slide 34: Detail Design - Node
A
B
B
A
B
A
B
A
Interface
Composition
Aggregation
Class
Use
Realize
Package
Legend

## Slide 35: Detail Design - Node(Responsibility Catalog)
Table D4. Element Responsibility Catalog for Node detail design
 | Perspective: Static
Element | Responsibilities
Service | Service is managing the core functionality of the running process.
View | Responsible for User Input & data presentation (Specially for UI scenerio)
LoginView | Responsible for User login (UI)
ConfigView | Responsilbe for Node & Server Remote Configuration (Like, Log Store Duration, Lighs Auto switch-off duration etc)
NodeControlView | Responsible for Remote Node Control Operation (UI)
RegisterNodeView | Resposible for New Node Registration & Existing Node UnRegistration (UI)

## Slide 36: Detail Design – Sequence diagram
Node registration
Service:Terminal
Request register
Broker:Server
Node manager:Server
Node manager:Server
Request register
Check new node
Find new node
Request register
Check serial
Node information
Node information
Register confirm
Register confirm

## Slide 37: Detail Design - Protocol
Command | Sender | Intermediacy | Receiver | Value
Certificate user |  |  |  | 
Request login | Terminal |  | Server | ID/PW
Confirm login | Server |  | Terminal | Success or Fail
Register node |  |  |  | 
Request registration | Terminal | Server | Node | serial
Confirm registration | Node | Server | Terminal | (success, nodeinfo) or (fail, reason)
Confirm registration | Server |  | Terminal | fail, reason
Get node value |  |  |  | 
Get node value | Terminal |  | Node | 
Node value response | Node |  | Server | node value
Node value response | Server |  | Terminal | All node value

## Slide 38: Detail Design – Mata data
Certificate user
Register node
Confirm
1st level | 2nd level | Type | value | 
messageType |  | string | register, etc | 
id |  | srring |  | 
password |  | string |  | 
1st level | 2nd level | Type | value | 
messageType |  | string | register, etc | 
serial |  | number |  | 
1st level | 2nd level | Type | value | 
messageType |  | string | register, etc | 
result |  | srring | success or fail | 
reason |  | string |  | 

## Slide 39: Detail Design – Home alarm status & operation
No
response
Alarmed
Normal
Send message
- Ask to set alarm
House is vacant
Set alarm
Release alarm
If door is opened,
Close door
Door is not opened
Door open by terminal
Send emergency message
Door is manually open
house is suddenly occupied
: State
A
: Transition state A to B
B
: Operation
response
Legend

## Slide 40: Test
Component test
  Developer has to make a test code to verify the component function & exceptional case
Integration Testing
  Check the interaction between components and process
End-to-End Testing
  Functional requirement and Quality attribute have to be satisfied
https://docs.google.com/spreadsheets/d/1CdMVoBw4cy1Zbp0Z8SkYRK1k3dqOfnMNZs8clBQGcMk/edit#gid=1975672019

## Slide 41: Project plan & Time log
 | -2W | -1W | 1W(5/25~) | 2W(6/1~) | 3W(6/8~) | 4W(6/15~) | 5W(6/22~)
Schedule |  |  |  |  |  |  | 
output |  | Initial presentation (Draft) | Initial presentation Project Context Architect Driver Project plan Time log |  | Prototype Demo Architectural design(Draft) |  | Presentation Architectural design Detail Design Test result Time log Demo
5/29
Initial presentation
Project analyze
Design
Implementation
Test
6/12
Prototype demo
6/26
Final presentation

## Slide 42: Project plan & Time log
Chart: 
| Development | Test | Planing | Analysis | Design | Prototype
 | 180 | 66 | 40 | 147 | 264 | 69
 |  | Plan(h) | Actual(h) | Gap(h)
Architect | Planing | 33 | 40 | 7
 | Analysis | 141 | 147 | 6
 | Design | 128 | 264 | 136
 | Experience | 54 | 69 | 15
Development | Detail design | 85 | 82 | -3
 | Implement | 96 | 98 | 2
Test | Test | 135 | 66 | -69
total |  | 672 | 766 | 94
Chart: 
| Planing | Analysis | Design | Experience | Detail design | Implement | Test
Planed time | 33 | 141 | 128 | 54 | 85 | 96 | 135
Actual time | 40 | 147 | 264 | 69 | 82 | 98 | 66
hour

## Slide 43: Future plan
Emerging protocol
  Bluetooth protocol will be supported by next handler release
Service provider for system stability
  IoT server

## Slide 44: Lessons & Learned

## Slide 45
Appendixs

## Slide 46: Appendix

## Slide 47: Appendix - Quality Attribute Scenario
Quality Attribute Scenario
ID | QA-01
Scenario | Installer can add and remove nodes to the system easily
Raw quality attribute | Usability
Stimulus | Add/Remove Node to/from the System(Server)
Source(s) of the stimulus | Node
Relevant environmental conditions | The System(Server) shall be always online
Architectural elements | System(Server)
System response | The SA Node list of the System(Server) has to be updated by Add/Remove Node Operation
Response measure(s) | Node should be Added/Deleted to/from the System(Server) without System(Server) restart

## Slide 48: Appendix - Quality Attribute Scenario
Quality Attribute Scenario
ID | QA-02
Scenario | System(Server) will be available always to do any IoT Based Operations
Raw quality attribute | Availability
Stimulus | Add/Remove Node to/from the System(Server) Terminal access to the Server
Source(s) of the stimulus | system(Server)
Relevant environmental conditions | The System(Server) shall be always online
Architectural elements | Terminal, System(Server) & Node
System response | Server Fault Detection & Recover the Server with Auto-Recovery
Response measure(s) | Server Shouldn’t be restarted & be available online 99.99%. Processing should be resume within 30 Sec.

## Slide 49: Appendix - Quality Attribute Scenario
Quality Attribute Scenario
ID | QA-03
Scenario | Do not allow unauthorized persons to register a sensor that they do not own (think of the apartment case where a neighbor might be able to “see” your sensor).
Raw quality attribute | Security
Stimulus | Request for registration SA nodes
Source(s) of the stimulus | Unauthorized person
Relevant environmental conditions | The system and SA nodes are working properly.
Architectural elements | The system and SA nodes
System response | SA nodes should NOT be registered and request should be denied.
Response measure(s) | Denial for registration SA nodes by unauthorized person SHOULD be guaranteed.

## Slide 50: Appendix - Quality Attribute Scenario
Quality Attribute Scenario
ID | QA-04
Scenario | Only the authorized person(Terminal) can access the home sensors/actuators or access any data generated by them, or any data stored in the system
Raw quality attribute | Security
Stimulus | Access the Node or data in the System(Server)
Source(s) of the stimulus | Terminal
Relevant environmental conditions | System(Server) should give the access only the Authorized Terminal & work properly
Architectural elements | Terminal , System(Server)
System response | System gives the access permission to the user for sensors/actuators
Response measure(s) | Authorized User(Terminal) can access the sensors/actuators or data in the System(Server)

## Slide 51: Appendix - Quality Attribute Scenario
Quality Attribute Scenario
ID | QA-05
Scenario | The system should be store sensor values and log all user commands for some period of time
Raw quality attribute | Reliability
Stimulus | sensor values & user commands
Source(s) of the stimulus | Nodes & terminal
Relevant environmental conditions | The system is working properly. The store service could be implemented and the area for store is served.
Architectural elements | System
System response | The sensor value and log have to be stored during configured value
Response measure(s) | After change the sensor value and user command, all changes have to be stored correctly during configured time

## Slide 52: Appendix - Quality Attribute Scenario
Quality Attribute Scenario
ID | QA-06
Scenario | The system should make it easy for application developers (private persons, VARs, or other 3rd parties) to build custom apps, services, and/or make mashups from existing available services (you should describe how the design supports this).
Raw quality attribute | Extensibility
Stimulus | Develop a custom application or service
Source(s) of the stimulus | Private persons, VARs, or other 3rd parties developers
Relevant environmental conditions | The system has been designed, implemented and working properly.
Architectural elements | Custom application, service or nodes
System response | 3rd party application can receive events from other nodes and access to data in our system by their permissions.
Response measure(s) | 3rd party application can control and interact with other nodes.

## Slide 53: Appendix - Quality Attribute Scenario
Quality Attribute Scenario
ID | QA-07
Scenario | The system should make it easy to add emerging protocols
Raw quality attribute | Modifiability
Stimulus | Supporting emerging protocol
Source(s) of the stimulus | System
Relevant environmental conditions | The system does not support the emerging protocol
Architectural elements | System
System response | The system can adapt emerging protocol without changing other protocol which is already supported.
Response measure(s) | When the node with emerging protocol is installed, it has to be added in the node list.

## Slide 54: Detail Design - Protocol
Command | Sender | Intermediacy | Receiver | Value
Certificate user |  |  |  | 
Request login | Terminal |  | Server | ID/PW
Confirm login | Server |  | Terminal | Success or Fail
Register node |  |  |  | 
Request registration | Terminal | Server | Node | serial
Confirm registration | Node | Server | Terminal | (success, nodeinfo) or (fail, reason)
Confirm registration | Server |  | Terminal | fail, reason
Get node value |  |  |  | 
Get node value | Terminal |  | Node | 
Node value response | Node |  | Server | node value
Node value response | Server |  | Terminal | All node value

## Slide 55: Detail Design – Protocol #2
Command | Sender | Intermediacy | Receiver | Value
Unregister node |  |  |  | 
Request unregistration | Terminal | Server | Node | nodeId
Confirm unregistration | Node | Server | Terminal | Success or Fail
Control acturator |  |  |  | 
Control acturator | Terminal | Server | Node | nodeId, name, value
Confirm control | Node | Server | Terminal | success or fail
Request logs |  |  |  | 
Request logs | Terminal |  | Server | 
Confirm logs | Server |  | Terminal | logs
Set alarm |  |  |  | 
Ask to set alarming | Node | Server | Terminal | 
Set alarm | Terminal | Server | Node | yes or no

## Slide 56: Detail Design – Protocol #3
Command | Sender | Intermediacy | Receiver | Parameter
Send message |  |  |  | 
Send message | Node | Server | Terminal | (emergency, reason) or (normal, reason)
Set alarm timer |  |  |  | 
Set alarm timer | Terminal | Server | Node | time

## Slide 57: Detail Design – Mata data
Certificate user
Register node
Confirm
1st level | 2nd level | Type | value | 
messageType |  | string | register, etc | 
id |  | srring |  | 
password |  | string |  | 
1st level | 2nd level | Type | value | 
messageType |  | string | register, etc | 
serial |  | number |  | 
1st level | 2nd level | Type | value | 
messageType |  | string | register, etc | 
result |  | srring | success or fail | 
reason |  | string |  | 

## Slide 58: Detail Design – Mata data #2
Node information
1st level | 2nd level | Type | value | Command
messageType |  | string | register, etc | 
deviceType |  | string | node or terminal | 
nodeName |  | string | node name | 
nodeId |  | number | MACAddress | last 4 digit
sensor |  | array |  | optional
 | name | string | sensor name | 
 | valueType | number or array | vender define | 
acturator |  | array |  | optional
 | name | string | acturator name | 
 | valueType | number or array | vender define | 

## Slide 59: Detail Design – Mata data #3
Get value response
Control acturator
1st level | 2nd level | Type | value | Command
messageType |  | string | register, etc | 
nodeId |  | number | MACAddress | 
equipmentType |  | string | sensor or acturator | 
name |  | string | sensor or acturator name | 
value |  | number or string | vender define | 
1st level | 2nd level | Type | value | Command
messageType |  | string | register, etc | 
name |  | string | sensor or acturator name | 
value |  | number or string | vender define |